## Slide 1
EDGE AI FOR SLEEP HEALTH · RESEARCH PROTOTYPE
Apnea screening that runs on the
device — and adapts to each patient
A tiny INT8 SpO₂ screener on a Renesas RA8P1 (Cortex-M85) that recalibrates itself every night without patient labels, and improves across a fleet by sharing calibration — not data.
+0.035 BA
out-of-sample gain, label-free
77 µs · ~2 KB
per session, on the MCU
Live on-board
1024×600 LCD dashboard
Simulation / research prototype — not a clinical device. No medical claims.
Notes: Title. Product-style opener. Lead with three proven wins: label-free +0.035 BA gain, tiny on-MCU cost, and a live on-board LCD dashboard. Research prototype, not clinical.

## Slide 2
THE PROBLEM
Sleep apnea is a screening bottleneck
Underdiagnosed at scale
Most obstructive sleep apnea goes undetected — people are never referred for a sleep study in the first place.
The gold standard doesn't scale
In-lab polysomnography is expensive, lab-bound and one-night — low throughput by construction.
At-home screening has hard constraints
Continuous, at-home monitoring needs inference that is cheap, low-power, private, and adapts to each patient.
The gap we target
Lab polysomnography
cart of sensors · clinician-scored · one night · high cost
On-device screener
one finger sensor · self-calibrating · every night · microcontroller-cheap
The problem
02 / 11

## Slide 3
THE SOLUTION
A screener that fits on a microcontroller — and gets better in the field
SpO₂-only INT8 MLP · 10→32→16→1 · 897 parameters, running on the RA8P1 Cortex-M85.
On-device inference
The whole model runs on the MCU — no cloud round-trip. 77 µs and ~2 KB per session, decisions bit-exact vs the host reference.
Label-free self-calibration
Each night the device recentres its own decision line from its unlabelled data — the source of the +0.035 balanced-accuracy gain.
Privacy-preserving federation
Devices pool calibration statistics — not recordings. No raw patient data leaves the device, and the fleet lifts BA by +0.048.
Positioning: the contribution is the embedded / real-time realization and its honest, measured performance — a deployable edge path, not a new ML algorithm.
The solution
03 / 11

## Slide 4
HOW IT WORKS
Sense → infer → self-calibrate → federate
SpO₂ signal
10 features
60 s / 30 s stride
INT8 MLP on Cortex-M85
10 → 32 → 16 → 1 · 897 params
Per-window verdict
APNEA
+ running AHI
(window proxy)
Per-session recalibration · on device
The device uses its own unlabelled night to recentre the decision threshold — no labels, no cloud. This is the +0.035 BA gain.
Fleet federation · privacy-preserving
Devices share calibration statistics only — never recordings. Pooling 1→70 devices adds +0.048 BA; pooling beats per-site.
Architecture
04 / 11

## Slide 5
RESULTS · WHAT WORKS
Self-calibration lifts accuracy on unseen patients — with no labels
SEALED COHORT · n = 25
+0.035
balanced accuracy, out of sample
0.7910 → 0.8256
95% CI [+0.0057, +0.0651] · excludes zero
Label-free matches the labelled reference (+0.0359) — dropping labels costs nothing.
Balanced accuracy on subjects nothing was tuned on
Chart: 
| Shipped model τ = 0.29 | Self-calibrated (label-free)
BA | 0.791 | 0.8256
Result — on-device calibration
05 / 11

## Slide 6
RESULTS · WHAT WORKS
A fleet learns together — without sharing patient data
Δ balanced accuracy as calibration is pooled across 1 → 70 devices
Chart: devices pooled
| 1 | 2 | 3 | 5 | 10 | 20 | 40 | 70
Δ BA vs 1 donor | 0 | 0.0325 | 0.0268 | 0.036 | 0.0442 | 0.0472 | 0.0489 | 0.0479
Saturates around 20–40 devices · pooling beats per-site at every donor count.
+0.048
BA from full-fleet pooling · CI [+0.036, +0.060]
Privacy by design
No raw patient data leaves the device. Only per-device calibration statistics are pooled into a shared reference — recordings stay local.
Pooled calibration, not model averaging — the effect is real and measured.
Result — federation
06 / 11

## Slide 7
RUNS ON REAL HARDWARE
Fast, tiny, and bit-exact on the RA8P1
77,429
cycles / session
≈ 77 µs @ 1 GHz — full recalibration
6,718
cycles / inference
≈ 6.71 µs @ 1 GHz — one window
~2 KB
RAM / session
bounded working set
Board decisions are bit-exact vs the host reference. The same INT8 pipeline gives the same answer on the MCU as on the workstation — verified over serial on hardware.
Cost is reported as cycles and RAM — an on-board current probe for a joules figure is on the roadmap.
On-device performance
07 / 11

## Slide 8
LIVE DEMO · NEW THIS SESSION
A working edge dashboard on the board
A night of SpO₂ data streams over serial into the RA8P1. The firmware runs the model per window and drives a 1024×600 LCD in real time — a big verdict, running AHI and live counts.
Built, flashed & serial-verified on hardware this session
An apnea window returns APNEA at prob 0.9673 — bit-exact vs host
Per-window updates: verdict, AHI window-proxy, live counts
APNEA SCREENER · RA8P1 · 1024×600
LIVE
APNEA
prob 0.9673
AHI
22.3
/h
APNEA
43
windows
NORMAL
180
windows
night progress
Live demo — on-board LCD dashboard
08 / 11

## Slide 9
WHY IT MATTERS
A deployable edge path for adaptive screening
Proven this project
Full model runs on a microcontroller — 77 µs, ~2 KB, bit-exact vs host.
Label-free per-session adaptation: +0.035 BA on unseen patients, no labels.
Privacy-preserving federation: +0.048 BA sharing statistics, not data.
A live on-board LCD dashboard, flashed and verified on hardware.
Where it fits
Cheap Commodity MCU + a finger SpO₂ sensor — no lab, no cart.
Private Inference and adaptation stay on-device; only statistics federate.
Adaptive Improves per patient every night, and per fleet over time.
Honest Every result reported with confidence intervals and measured cost.
Impact & positioning
09 / 11

## Slide 10
SCOPE & ROADMAP
Honest scope today — and the path to the clinic
What we show is real and measured. These are the next steps to clinic-readiness, not gaps in the demo.
Confirm the effect
Sealed n = 25, CI lower bound +0.0057 — promising but short of the pre-registered +0.02 bar.
Next → Widen the cohort to 100–200 subjects.
Clinical AHI scoring
Today AHI uses a window proxy, which is directionally unresolved.
Next → Score real respiratory-event durations.
Operating point vs ranking
The gain is at the decision threshold; AUROC (ranking) is unchanged by calibration.
Next → Add representation gains on top of calibration.
Energy budget
Cost is reported as cycles and RAM — no current probe yet.
Next → Add an inline probe for a joules figure.
NPU acceleration
The Ethos-U55 is present in silicon but unused — inference runs on the CPU.
Next → Offload inference to the NPU path.
Fleet field trial
The board has been exercised on a session for mechanism, cost and parity.
Next → Run a multi-device fleet in the field.
Scope & roadmap
10 / 11

## Slide 11
THE TAKEAWAY
Adaptive apnea screening —
proven on the device
+0.035 BA
label-free, out-of-sample
+0.048 BA
privacy-preserving fleet
77 µs · ~2 KB
bit-exact on the MCU
Live LCD
working on hardware
A deployable edge path — cheap, private, adaptive. Next: wider cohort, clinical AHI scoring, NPU offload, and a fleet field trial.
Simulation / research prototype — not a clinical device.
Notes: Close. Four proven wins plus a forward-looking roadmap. Deployable edge path. Not clinical.